## Slide 1: Socket Communication using AT+QIOPEN & AT+QISEND
K S SYAMKRISHNA

## Slide 2: What is Socket Communication?
Socket = endpoint for sending/receiving data over the internet
Used for:
  Remote sensor data upload
  Server communication
  MQTT, HTTP, FTP
  Works over TCP or UDP

## Slide 3: AT Command Flow Summary
Set APN using AT+CGDCONT
Activate PDP with AT+QIACT
Open socket: AT+QIOPEN
Send data: AT+QISEND
Close socket: AT+QICLOSE
Works on TCP and UDP

## Slide 4: Step 1 – Configure APN
AT+CGDCONT=1,"IP","jionet"
Replace "jionet" with your SIM provider’s APN

## Slide 5: Step 2 – Activate PDP Context
AT+QIACT=1
Enables internet context
Required before opening socket

## Slide 6: Step 3 – Open Socket with AT+QIOPEN
Syntax:
AT+QIOPEN=1,0,"TCP","<server>",<port>,0,1
1: PDP context ID
0: Socket ID (0–11)
"TCP": Type (TCP or UDP)
<server>: IP/domain of server
<port>: Server port
0: local port (0 = auto)
1: keep alive

## Slide 7: Step 3 – Open Socket with AT+QIOPEN
AT+QIOPEN=1,0,"TCP","example.com",80,0,1
Expected:
  OK
  +QIOPEN: 0,0 ← Success

## Slide 8: Step 4 – Send Data using AT+QISEND
Syntax: AT+QISEND=0,<length>
0: Socket ID
<length>: Number of bytes to send

## Slide 9: Step 4 – Send Data using AT+QISEND
AT+QISEND=0,18
Then:
    > GET / HTTP/1.1
    > Host: example.com
(CTRL + Z)
Response:
  SEND OK

## Slide 10: Receive Server Response
+QIURC: "recv",0,<len>
<response data>
Example: HTTP response or sensor acknowledgment

## Slide 11: Close the Socket
AT+QICLOSE=0
Frees up the module’s socket for future connections.

## Slide 12: Real world Use Cases
Remote IoT data upload (HTTP/MQTT)
Server-triggered SMS/alert actions
GPS tracking updates
Smart meters and utilities

## Slide 13: Recap
Use QIOPEN to open socket
Use QISEND to transmit data
Always close with QICLOSE
Reliable method for embedded internet communication